The tender texts below comprise the most common solutions in practice so that options and parts that are not required can be deleted and only quantities need to be inserted.

For certain projects it is recommended to edit the texts. Our experienced colleagues will be pleased to support you competently, quick and free of charge when it comes to create your tender texts. Please contact us via sales@nivus.com or by phone: +49 7262 9191-794.

NivuFlow Mobile 550

Portable flow rate measurement with extremely long

battery life independent from mains power, integrated

data logger and GPRS modem for remote data transmission,

limit value alerting and device diagnostics, suitable for

use and programming in Ex zone 1.

Flow rate measurement in full and part filled pipes and

any canal profile.

Detection of the water surface level as well as the

surface velocity

Flow transmitter with integrated numeric

discharge models for detection of average flow

velocity from individual velocities as measured 
on the surface.

Connection option and calculation functions for

single surface radar sensor for determination

of the accurate flow profile distribution in part filled 
pipes, channels and water body profiles.

Programming, representation of readings and data

transmission via secured, password-protected 
WLAN connection without the need to open the unit.

Programming optional via separate display and operation 
module Type ZAB 01 or via standard Smartphone,

Tablet or Laptop with Android, Windows or iOS.

Internal storage and transmission of all relevant

measurement data.

Storage of all readings in the transmitter.
Transmission of all relevant measurement data.

Delay-free and event-based detection of measurement

values including switchover of measurement cycles,

programmable via digital input, level limit value

threshold, flow velocity, flow rate or analogue input.

Options for continuous output of flow rate, flow

velocity or medium temperature on free scalable

analogue output.

Output of free programmable flow rate impulses,

event-related messages or limit values via digital output.

Integrated alarm management on exceeding/falling below

limit values and automatic additional data transmission

to the NIVUS WebPortal, triggered by

flow rate, level, average flow velocity and battery

voltage as well as for analogue inputs 1 and 2.

5 free programmable high and low limit values

Per measurement channel (Q, h, v, T, AI1, AI2).

5 free programmable low limit values for the

battery voltage

Reset of limit value violation through new automatic

data transmission, programmable by hysteresis

setting per measurement channel.

Direct report and automatic data transmission

through the digital input.

Automatic error message in case of sensor

interruption or short circuit.

Rugged, shock-proof, absolutely water-tight compact

plastic enclosure suitable for use in wastewater.

Redundant power supply thanks to 1 or 2 easily

replaceable gas-tight rechargeable batteries with double

plug-in connection.

Options for additional external power supply

via power adapter, solar panel, fuel cell,

extra batteries or similar.

Integrated LED visible from the outside for easy visual

identification of instrument status and error messages

without the need to open the transmitter

Modern, intuitive operation using external touchscreen.

Automatic sensor detection and indication of article no.,

serial no. and sensor type.

Reconciliation of the measurement system to improve

accuracy by automatically reading the calibrated

sensor-specific parameters.

Quick start assistant for easy initial programming

of the measurement place in dialogue mode.

Programming with flat hierarchical structure, supported

by colours and graphic elements, visual true-to-scale

representation even of complex canal shapes and sensor

positions in order to avoid errors during commissioning.

Error diagnostics related to sensor and time.

Integrated recorder function with min. and max. memory.

Storage of average flow velocity and flow rate in

internal high capacity memory.

Additional options to store up to 3 external analogue

signals such as level, overflow volumes, reference values

etc. as well as a digital input (counter, runtime).

Programming and all saved readings and errors can be

read out via WLAN or using an USB stick.

Protection:	IP 68 (closed)

IP 67 (lid open)

Ex Protection:	Zone 1 (optional)

Power Supply:	1/2 replaceable rechargeable lead

gel batteries, 12 V DC/15 Ah each

Internal Data	up to 182 000 data sets

Memory:

Max. Memory	20 years with 60-minute cycle

capacity:

Meas. modes:	Interval, constant, event

Interval, event, constant

Storage interval:	separately adjustable intervals for

normal and event operation.

Interval cycles:	5, 10, 15, 20 and 30 seconds

1, 3, 5, 10, 15, 20, 30 and 60 min.

Data transmission:	via WLAN, USB stick or

internal LTE modem (optional).

remote data transmission to

provided NIVUS WebPortal
(NIVUS-Connectivity, optional)

Inputs:	1x velocity radar sensor

2 x 0/4-20 mA (active)

1x 0/4-20 mA (passive)

1x digital input (active)

1x power adapter/alternative 
power supply

Outputs: 	1x voltage output 0-10 V

1x digital output (SPDT)

1x USB-A interface for
USB stick

Connection:	via water-tight, corrosion proof

IP 68 plug connectors.

Integrated automatic sensor detection

with article no., serial no., sensor type

and sensor parameters.

Material:	glass-fibre reinforced plastic

Weight:	approx. 2.2 Kg (without battery)

Version:	NFM-0550

Transmitter incl. memory stick, activation magnet and

screwdriver to open the battery compartment

Deliver including plugged NIVUS multi-roaming SIM card

with 1 year of free data transmission to the NIVUS

WebPortal.

Type: ............................

Make: .....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Data transmission fee for the NIVUS devices Type

NFM with integrated LTE modem and NLG.

Required tariff after the free 12-month data transmission 
included with the purchase of a new NFM or NLG

has expired.

Transmission of readings to the NIVUS WebPortal

or via NIVUS data kiosk to a customer system.

Shortest permissible

measurement cycle:	1 minute

Shortest permissible

transmission cycle:	1 hour

Period of notice:	3 months to the end of the

contract period

Total contract

period:	……… years

Version:	SNI0CONNECT01

Unlock for the device in use

Type: ............................

Make: .....................

Qty.:  1 	UP: ..................

TP: ....................

Licence Key

For device -related transmission of measurement 
data using a customer SIM card.

Transmission via FTP and/or e-mail to customer

server or free selectable e-mail address.

Provision of access data for NFM unlocking by

operator.

Version:	NFM0 LIZENZ FTP

Provision of access data by e-mail

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Gas-tight rechargeable battery with built-in double

plug-in connection for quick battery replacement.

Designed for long-term optimised power supply

of the portable NFM transmitter family.

Suitable for using the NFM in Ex areas

Zone 1 (optional)

Type:	lead gel

Voltage:	12 V DC

Capacity:	14 Ah

Weight:	approx. 4.0 kg/pc.

Versions:	NFM0 ZAPB 1215

NFM0 ZAPB 1215 E (Ex option)

Deliver

Type:............................

Make:.....................

Qty.:  2 Pcs.	UP: ..................

TP: ....................

Power adapter with charging tray for rechargeable

battery Type NFM0 ZAPB 1215 and as extra

power supply for NFM in non-Ex areas.

Version:	NFM0 ZLAD

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Display and operating module for NFM series

IP67-certified 8" outdoor tablet

on non-Ex areas.

Resolution:	1280 x 800

Operation:	Touchscreen

Operating system:	Android

Communication:	WLAN, USB, Bluetooth,

2G, 3G and 4G.

Version:	NFM0 ZAB0 1

Deliver and install ready to use according to

manufacturer's specifications

Type:............................

Make:.....................

Qty:  1 Pc.	UP: ..................

TP: ....................

Sensors

Surface flow velocity sensor Type OFR
for installation above the channel.

Surface flow velocity detection through

sensor-integrated radar sensor.

Sensor suitable for bidirectional surface velocity

measurement.

Measurement range:	-10 m/s to 10 m/s

Material:	plastic

Protection:	IP 68

Ex Protection:	Zone 1 (optional)

Versions:	OFR0 H00

OFR0 EVG (Ex version)

Deliver and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Connection cable for OFR sensor

Configured cable with IP 68 plugs on both ends

for connection to NivuFlow Mobile.

Cable length:	10 m (option: 15/20/30/50/70/100 m)

Version:	ZUB0 OFR NFM

Deliver, lay out and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Ultrasonic level sensor with integrated temperature

sensor to compensate ultrasound transit time and

built-in free programmable evaluation electronic.

Encapsulated, permanently immersible sensor in

corrosion-proof enclosure with high chemical

resistance.

Measurement range:	0.3 to 6 m

Meas. uncertainty:	4 mm over entire measurement range

Resolution:	2 mm

Startup time:	4 sec. until output of readings

Memory:	Flash

Calibration:	via HART

Enclosure:	Valox 357

Temperature range:	-50° to max. +80 °C

Fastening:	rear thread 1“

Protection:	IP 68

Ex Protection:	Ex ib for Zone 1 (optional)

Output:	4 - 20 mA / HART

Cable length:	10 m (optional: 10/20/30 m) with integrated

plug for connection to NFM

Version:	NMI0 06

Deliver, install ready to use according to manufacturer

specifications and set up according to application

Type:............................

Make:.....................

Quantity:  1 Pc.	UP: ..................

TP: ....................

Intrinsically safe T-shape antenna for remote data

transmission with fixed cable and water-tight 
IP 68 plug for direct connection to NFM 750.

Protection:	IP 68

Ex-Protection:	Ex ib for zone 1

Cable length:	2.5 m with integrated plug for
connection to NFM

Version:	NFM0 ZANT 1

Deliver, install and connect ready to use according 
to manufacturer specifications

Type: ............................

Make: .....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Instructions on handling, installation, setting of

parameters and data evaluation of NFM 550 under

real measurement place conditions

(if available and provided).

Duration:	6 hours

Qty.:  Flat Rate	UP: xxxxxxxxxxx

TP: ....................

Accessories

Combi holder for i6 sensor and surface radar

Type OFR with robust cover to reduce soiling
in case of being flooded.

Suitable for installation on vertical walls or 
mounting constructions.

Material:	1.4571 (AISI 316 Ti)

Version:	ZUB0 OFR MO LV6

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

NFM suspension device for fastening

on step irons

Material:	1.4571 (AISI 316 Ti)

Version:	NFM0 ZHAK NFM0 2

Deliver and install ready to use

Type: ............................

Make: .....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

NFM suspension device for fastening

on step irons incl. 2 integrated suspension brackets

for coiled sensor cables.

Material:	stainless steel 1.4571 (AISI 316 Ti)

Version:	NFM0 ZHAK NFM0 1

Deliver and install ready to use

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Hoop guards for mechanical protection of NFM connection

plugs in harsh environments such as shafts, canals,

industrial plants etc.

Suitable for additional fastening of a Connector Box Type

NFM0 ZVS1 or an Adapter Box Type NFM0 ZAB 2VKK.

Material:	stainless steel 1.4571 (AISI 316 Ti)

Version:	NFM0 ZSBL IRE

Deliver incl. fastening material and install on NFM

ready to use

Type:............................

Make:.....................

Qty.:  1 Pair	UP: ..................

TP: ....................

Connector Box for parallel connection of multiple

input and output signals as well as an alternative

power supply to NFM.

Robust, break-proof plastic box with connection

cable incl. plug for connection to NFM.

Material:	stainless steel 1.4571 (AISI 316Ti);

GFK, PU

Protection:	IP 67

Connections:	1 socket for alternative power

supply

4 cable glands for external signals

Cable length:	0.2 m with fixed and encapsulated plug

for direct connection to NFM

Version:	NFM0 ZVS1

Deliver incl. mounting plate for fastening on hoop guards

and install ready to use according to manufacturer

specifications

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

Pre-configured cable with plug and open

cable ends for alternative external NFM

power supply in non-Ex areas via solar panel, fuel

cell, external batteries, rechargeable batteries etc.

Plug protection:	IP67

Cable length:	5 m

Cable connection:	one side with pre-configured plug
	one side with open cable ends

Version:	NFM0 ZVER PS

Deliver

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: ..................

TP: ....................

WEB-Portal

Data remote transmission software

Device-related access for the web-based NIVUS

data collection system.

Data collection system with centralised data storage

and device communication.

Devices connecting with centre save readings and

status data in a centralised data bank.

Data security and availability according to current

IP security standards.

Transmitted readings are provided in the portal for

1 year and can be downloaded manually.

Device overview and device status are available in

the portal. Measurement spots can be localised on an

integrated map. Readings are saved in the data bank

using the recording frequency and can be recalled

by using an Internet browser.

The http server can be operated with any Internet browser

available on the market.

Type:............................

Make:.....................

Qty.:  1 Pc.	UP: part of the transmitter standard delivery